~ APPLICATION ~

1-thread portable sewing machine (stitch type 101) to close all types of bags: paper (single or multi-wall), woven or unwoven polypropylene, nett, polyethylene, burlap, cotton bags of any content.

This is the standard machine!!

~ NEW ADVANCED FEATURES ~

Improved cam: increased life time More resistant bushings: increased life time and improved lubrication Reinforced cam follower and improved cam follower pin: no longer affected by bag jams! Enhanced needle lever assembly Faster double insulated motor with cooling fins

~ FEATURES ~

MECHANIC: The Portable is equipped with following components: Mechanical chain scissors cutting Semi-automatic lubrication system Presser foot lifter mechanism Corrosion resistant – epoxy paint Stitch length: Standard 7 mm, not adjustable Linear speed: around 13,6 m/min. (depends on the material and voltage) Maximum material thickness = 7 mm Noise level: 79 dB Vibrations: daily exposure values may not exceed 180 laps/h over a period of 8 h (1 work shift) – Bag width: 55cm ELECTRIC: Voltage: 230 V single phase Frequency: 50-60 Hz Power: 90 W - 0,75 A Motor: double insulated, class 2 without ground wire (not allowed). IP65 - 10.000 rpm (ref. 67753) Adequate lead wire PNEUMATIC: Not applicable.

~ PACKING ~

| Reference | Type of packing. | Dimensions | Net weight | Gross weight |
| --- | --- | --- | --- | --- |
| 50224F | Carton | L 38 x W 30 x H 34 cm | 5,8 kg | 7,2 kg |
| - | 18 units on a pallet shrink wrapped | L 93 x W 78 x H 113 cm | 104,4 kg | 140,6 kg |

| Custom tariff: | 8452.2900 |
| --- | --- |